## Slide 1: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
GROUP - III
Members
Outlines of Presentation
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
1

## Slide 2: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
GROUP - III
Members
Outlines of Presentation
Background story
Abstract
Datasets
Methods
Evaluation
Results
Discussion
What is preterm birth?
Effects of preterm birth?
Create monitoring system
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
2

## Slide 3: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Background Story
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
3

## Slide 4: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Abstract
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
Three classes that focus on . . .
4

## Slide 5: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Datasets
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
RGB Datasets | Thermal Datasets
An RGB Camera (UI-3860LE-C-HQ) | Three thermal cameras (FLIR Lepton 2.5)
Resolution 1280 x 720 pixels - 10fps | Resolution of 60 x 80 pixels - 9 fps
Placed on top of the incubator | Placed around the infants’ beds
To capture the head and upper body | Merged to observe infants from different directions simultaneously
9-hour videos from 5 infants | 32-hour thermal videos from 13 infants
Mean PMA of 31.2 (2.1) weeks | mean PMA of 36.7 (3.3) weeks
Three classes that focus on . . .
Four methods are . . .
Background Substruction (BS)
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
Oriented FAST and Rotated BRIEF (ORB).
5

## Slide 6: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Methods
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
RGB Datasets | Thermal Datasets
An RGB Camera (UI-3860LE-C-HQ) | Three thermal cameras (FLIR Lepton 2.5)
Resolution 1280 x 720 pixels - 10fps | Resolution of 60 x 80 pixels - 9 fps
Placed on top of the incubator | Placed around the infants’ beds
To capture the head and upper body | Merged to observe infants from different directions simultaneously
9-hour videos from 5 infants | 32-hour thermal videos from 13 infants
Mean PMA of 31.2 (2.1) weeks | mean PMA of 36.7 (3.3) weeks
Three classes that focus on . . .
Four methods are . . .
Background Substruction (BS)
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
Oriented FAST and Rotated BRIEF (ORB).
Before apply to each methods,
Each frame was transformed into a grayscale image and normalized by a histogram equalization to improve efficiency and contrast.
6

## Slide 7: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Methods
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
RGB Datasets | Thermal Datasets
An RGB Camera (UI-3860LE-C-HQ) | Three thermal cameras (FLIR Lepton 2.5)
Resolution 1280 x 720 pixels - 10fps | Resolution of 60 x 80 pixels - 9 fps
Placed on top of the incubator | Placed around the infants’ beds
To capture the head and upper body | Merged to observe infants from different directions simultaneously
9-hour videos from 5 infants | 32-hour thermal videos from 13 infants
Mean PMA of 31.2 (2.1) weeks | mean PMA of 36.7 (3.3) weeks
Three classes that focus on . . .
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
Oriented FAST and Rotated BRIEF (ORB).
Background Substruction (BS)
Before apply to each methods,
Each frame was transformed into a grayscale image and normalized by a histogram equalization to improve efficiency and contrast.
The BS method uses the difference between the current frame and a defined background model to detect the motion. The background model is needed to update to adapt to the impact of the changing external environment such as light.
THRESHOLD
Foreground mask
Background model
Current frame
7

## Slide 8: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Methods
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
RGB Datasets | Thermal Datasets
An RGB Camera (UI-3860LE-C-HQ) | Three thermal cameras (FLIR Lepton 2.5)
Resolution 1280 x 720 pixels - 10fps | Resolution of 60 x 80 pixels - 9 fps
Placed on top of the incubator | Placed around the infants’ beds
To capture the head and upper body | Merged to observe infants from different directions simultaneously
9-hour videos from 5 infants | 32-hour thermal videos from 13 infants
Mean PMA of 31.2 (2.1) weeks | mean PMA of 36.7 (3.3) weeks
Three classes that focus on . . .
Oriented FAST and Rotated BRIEF (ORB).
Background Substruction (BS)
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
The optical flow method uses the change of tracking points (motion vector with direction) between consecutive frames to detect motion. Depending on the density of pixels that are tracked by the optical flow method, the method can be categorized into SOF and DOF. SOF only need to compute optical flow of some pixels(features, corners of interest object) from the whole image, DOF computes all the pixels.
(A)Sparse optical flow
(A)Dense optical flow
8

## Slide 9: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Methods
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
RGB Datasets | Thermal Datasets
An RGB Camera (UI-3860LE-C-HQ) | Three thermal cameras (FLIR Lepton 2.5)
Resolution 1280 x 720 pixels - 10fps | Resolution of 60 x 80 pixels - 9 fps
Placed on top of the incubator | Placed around the infants’ beds
To capture the head and upper body | Merged to observe infants from different directions simultaneously
9-hour videos from 5 infants | 32-hour thermal videos from 13 infants
Mean PMA of 31.2 (2.1) weeks | mean PMA of 36.7 (3.3) weeks
Three classes that focus on . . .
Background Substruction (BS)
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
Oriented FAST and Rotated BRIEF (ORB).
ORB first find features.( finds pixels that are significantly different from neighbor pixels in a frame as tracking points.) Afterwards, these tracking points in two consecutive frames are compared whether it is matched or not.
9

## Slide 10: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Evaluation
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
Two experiment-motion detection & Gross motion detection.
Motion Detection is a combination of Gross motion and fine motion.
Gross Motion Detection is only gross motion.
Using Python 3.8.3 with opencv-contrib-python 4.5.5.62 (CPU-only)
on a CPU of 2.60GHz (Intel Core i7-9750H)
with no architecture specific instruction.
Background Substruction (BS)
Sparse Optical Flow (SOF)
Dense Optical Flow (DOF)
Oriented FAST and Rotated BRIEF (ORB).
ORB first find features.( finds pixels that are significantly different from neighbor pixels in a frame as tracking points.) Afterwards, these tracking points in two consecutive frames are compared whether it is matched or not.
In the thermal dataset, BS outperforms the other methods with mean (SD) AUCs of 0.86 (0.03) and 0.93 (0.03) for both experiments.
In the RGB dataset, SOF performs best for motion detection and is as good as DOF when detecting gross motion.
The performance of SOF and ORB increases with higher video resolution, but has little influence on the performance of DOF.
The run time does not differ per method for the thermal data, which has a low resolution.
In the RGB dataset, the run time is always higher, particularly the run time of DOF increases largely at high resolution.
10

## Slide 11: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
Two experiment-motion detection & Gross motion detection.
Motion Detection is a combination of Gross motion and fine motion.
Gross Motion Dection is only gross motion.
Using Python 3.8.3 with opencv-contrib-python 4.5.5.62 (CPU-only)
on a CPU of 2.60GHz (Intel Core i7-9750H)
with no architecture specific instruction.
Results
In the thermal dataset, BS outperforms the other methods with mean (SD) AUCs of 0.86 (0.03) and 0.93 (0.03) for both experiments.
In the RGB dataset, SOF performs best for motion detection and is as good as DOF when detecting gross motion.
The performance of SOF and ORB increases with higher video resolution, but has little influence on the performance of DOF.
The run time does not differ per method for the thermal data, which has a low resolution.
In the RGB dataset, the run time is always higher, particularly the run time of DOF increases largely at high resolution.
Method | Motion Detection | Gross Motion Detection | Run Time (ms)
BS | 0.76 (0.13) | 0.89 (0.04) | 30.0 (1.80)
SOF | 0.82 (0.09) | 0.91 (0.05) | 28.9 (2.65)
DOF | 0.79 ( 0.11) | 0.91 (0.05) | 234 ( 3.40)
ORB | 0.77 (0.11) | 0.84 (0.06) | 36.2 (1.10)
Method | Motion Detection | Gross Motion Detection | Run Time (ms)
BS | 0.86 (0.03) | 0.93 (0.03) | 16.0 (0.05)
SOF | 0.74 (0.06) | 0.87 (0.07) | 15.9 ( 0.05)
DOF | 0.78 ( 0.09) | 0.91 ( 0.05) | 15.8 ( 0.64)
ORB | 0.70 ( 0.11) | 0.81 ( 0.10) | 15.6 (0.02)
R G B
Thermal
11

## Slide 12: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
Two experiment-motion detection & Gross motion detection.
Motion Detection is a combination of Gross motion and fine motion.
Gross Motion Dection is only gross motion.
Using Python 3.8.3 with opencv-contrib-python 4.5.5.62 (CPU-only)
on a CPU of 2.60GHz (Intel Core i7-9750H)
with no architecture specific instruction.
Discussion
All the methods can capture gross motion well based on differences between two consecutive frames.
Why these methods are low performance in fine motion detection?
The BS method perform best in thermal videos, but the performance decreases in RGB videos.
BS & DOF cannot benefit from the increased resolution, but SOF and ORB can benefit.
The run time of the DOF method increases much more than other methods when running in high-resolution RGB videos.
These results can differ according to limitations of patient population and available views between the two datasets , and can make further research.
In the thermal dataset, BS outperforms the other methods with mean (SD) AUCs of 0.86 (0.03) and 0.93 (0.03) for both experiments.
In the RGB dataset, SOF performs best for motion detection and is as good as DOF when detecting gross motion.
The performance of SOF and ORB increases with higher video resolution, but has little influence on the performance of DOF.
The run time does not differ per method for the thermal data, which has a low resolution.
In the RGB dataset, the run time is always higher, particularly the run time of DOF increases largely at high resolution.
12

## Slide 13: A Comparison of Video-based Methods
For Neonatal Body Motion Detection
2022 44th Annual International Conference of
the IEEE Engineering in Medicine & Biology Society (EMBC)
Scottish Event Campus, Glasgow, UK, July 11-15, 2022
GROUP - 3
Members
Outlines of Presentation
What is preterm birth?
Effects of preterm birth?
Create monitoring system
Mg Thwin Htoo Aung 5IST-1
Mg Ye Win Htet 5IST-11
Mg Chan Min Ko 5IST-12
Mg Mabu Phong 5IST-13
Ma Khine Thet Thet Zaw 5IST-16
Background story
Abstract
Datasets
Methods
Results
Discussion
To compare the performance and
the computation time of
four video-based methods
for motion detection in preterm
infants, including BS, SOF, DOF, and ORB.
Two experiment-motion detection & Gross motion detection.
Motion Detection is a combination of Gross motion and fine motion.
Gross Motion Dection is only gross motion.
Using Python 3.8.3 with opencv-contrib-python 4.5.5.62 (CPU-only)
on a CPU of 2.60GHz (Intel Core i7-9750H)
with no architecture specific instruction.
In the thermal dataset, BS outperforms the other methods with mean (SD) AUCs of 0.86 (0.03) and 0.93 (0.03) for both experiments.
In the RGB dataset, SOF performs best for motion detection and is as good as DOF when detecting gross motion.
The performance of SOF and ORB increases with higher video resolution, but has little influence on the performance of DOF.
The run time does not differ per method for the thermal data, which has a low resolution.
In the RGB dataset, the run time is always higher, particularly the run time of DOF increases largely at high resolution.
All the methods can capture gross motion well based on differences between two consecutive frames.
Why these methods are low performance in fine motion detection?
The BS method perform best in thermal videos, but the performance decreases in RGB videos.
BS & DOF cannot benefit from the increased resolution, but SOF and ORB can benefit.
The run time of the DOF method increases much more than other methods when running in high-resolution RGB videos.
These results can differ according to limitations of patient population and available views between the two datasets , and can make further research.
Thank you
For your attention
?
13